## Slide 1: Canary SRAM Built in Self Test for SRAM Write VMIN Tracking
ECE 7502 Class Final Presentation
Arijit Banerjee
21th Apr 2015

## Slide 2
Requirements
Specification
Architecture
Logic / Circuits
Physical Design
Fabrication
Manufacturing Test
Packaging Test
PCB Test
System Test
PCB Architecture
PCB Circuits
PCB Physical Design
PCB Fabrication
Design and Test Development
Customer
Validate
Verify
Verify
Test
Test

## Slide 3: Outline
Problem statement: Testing of canary SRAMs with reverse assist
Expected outcomes
Approach: proposed canary built in self test (BIST)
Results
Conclusions

## Slide 4: Canary SRAM
An SRAM sensor that can be sensitive to retention, read, write
  Uses a reverse assist to degrade operations
Canary data retention voltage (DRV) tracking [Wang et al 2007]
Canary write minimum operating voltage (VMIN ) tracking [Banerjee et al 2014]
  Uses BIST to count the # of bit failures
  User knobs: failure threshold and degree of reverse assist

## Slide 5: Problem Statement: Testing of Canary SRAMs with Reverse Assist
Challenges in testing of canary SRAM
  Need to test canaries for a specific trend for bit failure vs. canary reverse assist at speed
  Testing should provide production go no-go and diagnostic data of the canaries
  Also the canary test hardware should have some testing capability of itself
How to check the functionality of the canary SRAM with reverse assist so that it can be used to track SRAM write VMIN?
To develop a canary BIST (CBIST) that can test the failure trends in canary at speed in production run and also provide the failure diagnostic data for the canary SRAM

## Slide 6: Expected Outcomes
To design a CBIST in Verilog and synthesize it in IBM 130nm technology for a 512bit canary with reverse assist
  To check the trend to be within a max and min bit failure rate (BFR) limit and monotonicity of the failure data
  To run at speed covering all the reverse assist settings for write 0 and write 1 trends
  Will have go no-go production CBIST run support and debug functionality for each reverse assist settings
Equip CBIST with some design for testability (DFT) feature for testing itself and estimate its test and fault coverage
  Full scan insertion
  Estimation of fault coverage using stuck at transition fault models

## Slide 7: Approach: Proposed Canary BIST Architecture
Verilog entry of the CBIST for a 512b canary SRAM consisting of three blocks
  CBIST finite state machine (FSM)
  CBIST bit failure rate (BFR) FSM
  BFR table to min and max BFR interface

## Slide 8: Approach: CBIST FSM Algorithm
CBIST FSM controls the canary SRAM with reverse assist and BFR FSM
Generates read-write signals, canary address and data in values
Initializes canary SRAM without reverse assist using Init-word
Then writes !Init-word and reads back
Covers all RaSel settings and for write 0 and write 1

## Slide 9: Approach: CBIST BFR FSM Algorithm
CBIST BFR FSM calculates the bit failures per BIST run of canary SRAM
Covers all the reverse assist settings (RaSel)
Also checks the monotonicity of the BFR data with RaSel values

## Slide 10: Approach: Rest of the Design Verification and Test Generation Flow
RTL Verification of CBIST using Synopsys’s VCS simulator in DVE environment
Synthesis using Synopsys's Design Compiler
Post synthesis design verification using VCS
DFT Scan Insertion in CBIST using Synopsys’s DFT compiler
Synopsys’s TetraMAX fault simulation of the CBIST using stuck at and transition fault models for test coverage

## Slide 11: Results: Pre-Synthesis RTL Fault Simulation Results Minimum Case
Generated pre-determined total stuck at faults across reverse assist settings manually
Distributed the total faults randomly across the canary SRAM using Perl
Injected the pre-generated faults through RTL testbench
Matching signatures after CBIST run
BIST Done and Go signal asserted
CBIST running for different reverse assist settings

## Slide 12: Results: Post-Synthesis RTL Fault Simulation Results Pass Case
Synthesized using IBM 130nm at SS_1.08V_-55C corner with 36ns (27.77MHz) Clock period
Able to detect BFR scenarios
  Nominal
  Minimum
  Maximum
Minimum BFR Case Output:
Calc BFR Signature is: 6e1684108c0c80a000006e1684108c0c80a00000
Read BFR Signature is: 6e1684108c0c80a000006e1684108c0c80a00000
BIST Go No Go Status is: 1
BIST Status Register Value is: ffff
Chart: Max, Min, Nominal Write Bit Failure Rate vs. Reverse Assist Settings
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Typical BFR | 1 | 5 | 40 | 140 | 260 | 390 | 470 | 512
Max BFR | 1 | 20 | 100 | 240 | 380 | 480 | 512 | 512
Min BFR | 0 | 0 | 10 | 50 | 140 | 260 | 360 | 440

## Slide 13: Results: Post-Synthesis RTL Fault Simulation Results Fail Case
Chart: Faulty Write Bit Failure Rate vs. Reverse Assist Settings
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Typical BFR | 1 | 5 | 40 | 140 | 260 | 390 | 470 | 512
Max BFR | 1 | 20 | 100 | 240 | 380 | 480 | 512 | 512
Min BFR | 0 | 0 | 10 | 50 | 140 | 260 | 360 | 440
Faulty BFR Case 1 | 1 | 70 | 190 | 300 | 440 | 512 | 512 | 512
Faulty BFR Case 2 | 0 | 0 | 1 | 10 | 120 | 210 | 312 | 430
Faulty BFR Case 3 | 0 | 23 | 14 | 120 | 340 | 290 | 400 | 490
Able to detect BFR scenarios
  Overshoot
  Undershoot
  Non-monotonic
Signature comparison shows error in BIST Status register
Faulty BFR Case 3:
Calc BFR Signature is: 7a990489541e00e05c007a990489541e00e05c00
Read BFR Signature is: 7a990489541e00e05c007a990489541e00e05c00
BIST Go No Go Status is: 0
BIST Status Register Value is: d9d9
1101 1001 1101 1001

## Slide 14: Results: Scan Insertion
Used Synopsys’s DFT Compiler
  Full scan chain
Estimated test coverage was 99.6%, however had issues in scan insertion and design rule check (DRC) errors were there that can cause fault simulation issue
Source: Dilip Vasudevan’s PhD thesis and a PPT from Kate, Yu-Jen Huang for DFT

## Slide 15: Results: Test and Fault Coverage
Used Synopsys TetraMAX
  Sequential full scan ATPG simulation
  Fault models: stuck at and transition
  Run in two different machines: thecorner and humpback
Stuck at fault coverage of collapsed faults was less than expected
  Thecorner <74.31%
  Humpback < 69.89%

## Slide 16: Results: Test and Fault Coverage
Transition fault coverage of collapsed faults was less than expected
  Thecorner < 64.74%
  Humpback < 64.56%
  Possible issue is DRC error which occurred during the scan insertion
  Did not got time to dig into it for a fix

## Slide 17: Timeline
Deliverables | Expected Date | Projected Date | Actual Date | Status | Issues
Architecture and Algorithm Design for CBIST | 2/16/2015 |  | 2/16/2015 | Done | none
Verilog entry of scan chain to BFR data table interface and simulation results | 2/26/2015 |  | 2/26/2015 | Done | Having Verilog compilation issues initially, but resolved later.
Verilog entry of CBIST FSM and simulation results | 3/4/2015 |  | 03/4/2015 | Done | NA
Verilog entry of CBIST bitwise XOR, bit adder and error accumulator FSM and simulation results | 3/11/2015 |  | 03/9/2015 | Done | NA
Canary SRAM to CBIST interface and full RTL integration for canary BIST in Verilog and simulation results | 3/18/2015 | 3/25/2015 | 04/14/2015 | Done | Delayed due to time crunch. Will catch up soon and complete.
Synthesis of Full CBIST using DC in IBM 130nm | 3/25/2015 | 3/27/2015 | 04/14/2015 | Done | Schedule changed. Will do that on 25th March week

## Slide 18: Timeline Continued
Deliverables | Expected Date | Projected Date | Actual Date | Status | Issues
Post synthesis verification of the CBIST | 3/30/2015 |  | 04/14/2015 | Done | Time issues
SPICE / DVE Simulation results of CBIST pass/fail testing and test access time | 4/01/2015 |  | 04/14/2015 | Done | Time issues
Modeling the canary SRAM for stuck at and canary BIST for delay faults | 4/07/2015 |  | 04/14/2015 | Done | Time issues
Canary BIST Fault coverage results using TetraMAX | 4/14/2015 |  | 04/14/2015 | Done | Time issues
Final Project Report | 4/28/2015 |  |  | Ongoing | 

## Slide 19: Conclusions
The CBIST design shows promises to solves the issue of canary testing to see if canary with reverse assist can be used to track SRAM write VMIN.
We here only focused on canary write failure trend checking, but this hardware can be extended to readability testing also
Speed of the CBIST is not so good as the functionality is heavy and technology is 130nm
Scan insertion was a bit troublesome and had DFT DRC issues
Overall timeline was met successfully and the project was successful

## Slide 20: References
[1] J. Wang and B. Calhoun, “Canary replica feedback for near-DRV standby vdd scaling in a 90 nm SRAM,” in Proc. Custom Integrated Circuit Conf. (CICC ’07), Sep. 2007, pp. 29–32.
[2] Banerjee, A.; Sinangil, M.E.; Poulton, J.; Gray, C.T.; Calhoun, B.H., "A reverse write assist circuit for SRAM dynamic write VMIN tracking using canary SRAMs," Quality Electronic Design (ISQED), 2014 15th International Symposium on , vol., no., pp.1,8, 3-5 March 2014
[3] B. Zimmer, S. O. Toh, H. Vo, Y. Lee, O. Thomas, K. Asanovic, and B. Nikolic, “SRAM assist techniques for operation in a wide voltage range in 28 nm CMOS,” IEEE Trans. Circuits Syst. II, vol. 59, no. 12, pp. 853– 857, Dec. 2012.
[4] Fradi, A.; Nicolaidis, M.; Anghel, L., "Memory BIST with address programmability," On-Line Testing Symposium (IOLTS), 2011 IEEE 17th International , vol., no., pp.79,85, 13-15 July 2011
[5] Zarrineh, K.; Upadhyaya, S.J., "Programmable memory BIST and a new synthesis framework," Fault-Tolerant Computing, 1999. Digest of Papers. Twenty-Ninth Annual International Symposium on , vol., no., pp.352,355, 15-18 June 1999
[6] Kokrady, A.; Ravikumar, C.P.; Chandrachoodan, N., "Layout-Aware and Programmable Memory BIST Synthesis for Nanoscale System-on-Chip Designs," Asian Test Symposium, 2008. ATS '08. 17th , vol., no., pp.351,356, 24-27 Nov. 2008
[7] Ching-Hong Tsai; Cheng-Wen Wu, "Processor-programmable memory BIST for bus-connected embedded memories," Design Automation Conference, 2001. Proceedings of the ASP-DAC 2001. Asia and South Pacific , vol., no., pp.325,330, 2001